## Slide 1: Good Morning! 早上好! 안녕하세요!
Day 4

## Slide 2: Day 1
Welcome
Project Introduction
Introduction to Project Development Process
Business Requirement Development
System Requirement Development
System(High Level) Design
Time Management

## Slide 3: Day 2 (Mini project)
Yolo객체 인식 모델 활용과 성능 평가 방법 이해
Custom Dataset과 Fine Tuning으로 자체 객체 인식 모델 구현 및 평가
(Optional)Segmentation,Tracking,경량화 모델 등 개별 요구사항에 적합한 모델 탐색 및 성능 검증
YOLOv8 기반 데이터 수집/학습/deploy (Detection Alert)
  감시용 데이터 수집(bus, truck, tank 등)
  감시용 데이터 라벨링
  YOLOv8 기반 학습
  YOLOv8 Object Detection
Porting to ROS
  Create Detection Alert Node
  Generate Topics to send image and Obj. Det. results
  Create Subscriber node and display image and print data from the Topic

## Slide 4: Day 3 (Mini project)
AMR(Autonomous Mobile Robot) Turtlebot4 개발 환경 구축
로봇 개발 환경에 완성 모델 서빙 및 테스트 / 로봇 H/W, 제반 환경의 한계점 도출
  Tracking 데이터 수집(bus, truck, tank 등)
  Tracking 데이터 라벨링
  YOLOv8 기반 학습
  YOLOv8 Object Tracking
Turtlebot4 시뮬레이션 환경 구축
  SLAM과 Map 생성 및 파라미터 튜닝(Localization, AMCL)
  AutoSLAM으로 맵 생성

## Slide 5: Day 4 (Mini project)
Turtlebot4 Navigation과 파라미터 튜닝(Local Costmap, Global Costmap)
Turtlebot4 API를 활용한 Initial Pose Navigate_to Pose 구현
Turtlebot4 API를 활용한 Navigate_Through_pose, Follow Waypoints 구현
로봇 개발 환경에 적용 및 테스트 / 로봇 H/W, 제반 환경의 한계점 도출
AMR기반 카메라 인식 autonomous driving 시스템 with obstacle avoidance 구축 (AMR Controller)
  Digital Mapping of environment
  Goal Setting and Obstacle Avoidance using Navigation
  Object Tracking w/ AMR camera
  Control logic between navigation/obj. tracking/ obj. following (teleop)
Porting to ROS
  Create AMR Controller Node
  Create and send Obj. Tracking Image and data to Sysmon
Integrate and test with Detection

## Slide 6: Day 5 (Mini project)
Flask 를 이용한 웹 서버 구축 (System Monitor)
  Flask/HTML Intro
  Deploy YOLOv8 Obj. Det results to web
  Log in 기능 구현
  Sysmon 웹기능 구현
  알람 기능 구현
SQLite3를 이용한 데이터베이스 구축 및 연동 (System Monitor)
  SQLite3 기본 기능 구현
  DB 기능 구축
  알람이 울리는 경우 DB에 저장하는 기능 구현
  저장된 내용 검색하는 기능 구현

## Slide 7: Day 5 (Mini project)
Porting to ROS
  Update Sysmon Node code
  Update the database with received Obj. Det. Data from Detection Alert Node
  Display the content of DB on System Monitor web page
And finally, Integration and Test of Detection Alert & System Monitor

## Slide 8: 프로젝트 rule number ONE!!!
Have Fun Fun Fun!

## Slide 11: SW Development Process
Agile-SPRINTs

## Slide 12: Project Sprints
Detection Alert
  Camera Capture
  Object Detection
  Send messages to other subsystems
AMR Controller
  Receive messages and act accordingly
  Move using (SLAM) with Obstruction avoidance
  Target Acquisition (Obj. Det.) and Tracking
  Follow target using camera and motor control
System Monitor
  Receive and Display Detection Camera and info
  Receive and Display AMR Camera and info
  Store, display, and report Information and Alerts

## Slide 13: Team Exercise 5
Perform coding and testing of Detection Alert Module

## Slide 14: Results & Code Review by each team
Show actual results against the expected results and explain the code written

## Slide 15: Project Sprints
Detection Alert
  Camera Capture
  Object Detection
  Send messages to other subsystems
AMR Controller
  Receive messages and act accordingly
  Move using (SLAM) with Obstruction avoidance
  Target Acquisition (Obj. Det.) and Tracking
  Follow target using camera and motor control
System Monitor
  Receive and Display Detection Camera and info
  Receive and Display AMR Camera and info
  Store, display, and report Information and Alerts

## Slide 16: Running in simulation

## Slide 17: Simulation Summary
Topics
Sensors
Teleops
SLAM
Navigation

## Slide 18: Controlling actual robot

## Slide 19: AMR Introduction
User Manual · Turtlebot4 User Manual
https://turtlebot.github.io/turtlebot4-user-manual/

## Slide 20: Object Tracking with AMR Camera
Summary
  Data Collection
  PreProcessing
  Training
  Inferences
  ROSify

## Slide 21: Controlling the AMR Movement
Teleop with keyboard
Navigation with SLAM

## Slide 22: Using teleop
Robot_LiDAR_Camera_Depth Camera
https://www.notion.so/Robot_LiDAR_Camera_Depth-Camera-1cf450ef7c59805f8dcecaa3a5b1c8ce
NEED TO UPDATE

## Slide 23: digital Mapping (SLAM)
Robot_SLAM
https://www.notion.so/Robot_SLAM-1c1450ef7c598003aa8fccf98001fe78
NEED TO UPDATE

## Slide 24: digital Mapping (Auto – SLAM)
Robot_SLAM_explore_lite
https://www.notion.so/Robot_SLAM_explore_lite-1cf450ef7c5980ee9300d86a1ccb4afa
NEED TO UPDATE

## Slide 25: Digital Mapping
Check if correct
xdg-open <map-path>/map.pgm
Or,
eog <map-path>/map.pgm

## Slide 26: Navigation w/ map
Robot_Navigation
https://www.notion.so/Robot_Navigation-1cf450ef7c59802eb4befdfc4b2cea12
NEED TO UPDATE

## Slide 27: Parameter tuning???
slam
navigation
NEED TO UPDATE

## Slide 28: AMR controller sprint

## Slide 29: Sprint 2 – AMR controller

## Slide 30: Team Exercise 6
Perform Detail Design of AMR Controller Module using Process Flow Diagram

## Slide 31: Design hint
Initial Pose
  nav2
  rviz2 – 2D estimate pose
  ros2 topic echo /initialpose
How do you find AMR current position and orientation?
Sending Goals
  nav2
  Rviz2 – send goals
    ActionClient
    NavigateToPose.send_goal_async()
Stopping Navigation NavigateToPose.cancel_all_goals_async()
Sending multiple goals
  ActionClient
  /follow_waypoints
Manual control of AMR Odometry
  How to move forward, backward, left and right???
NEED TO UPDATE

## Slide 32: What is the follow Algorithm?
Left/Right?
Forward/Backward?
Velocity?
Camera position?
Depth? Local/Global Coordinate transform?

## Slide 33: Detail Design Review by each team
Using the process flow diagram present team’s design

## Slide 34: Sprint 2 – AMR controller

## Slide 35: Coding hint
Initial Pose
  nav2
  rviz2 – 2D estimate pose
  ros2 topic echo /initialpose
Sending Goals
  nav2
  Rviz2 – send goals
    ActionClient
    NavigateToPose.send_goal_async()
  ros2 topic echo /amcl_pose
Stopping Navigation
  ActionClient
  NavigateToPose.cancel_all_goals_async()
Sending multiple goals
  ActionClient
  /follow_waypoints
Manual control of AMR Odometry
  Twist
  /cmd-vel
NEED TO UPDATE

## Slide 36: Expected outcome
AMR navigates to avoid obstacles, ignores dummies, track, and follow target

## Slide 37: Sprint 2 – AMR controller

## Slide 38: Team Exercise 7
Perform coding and testing of AMR Controller Module

## Slide 39: Coding hint
NEED TO UPDATE

## Slide 40: Using TurtleSIM to test following logic
Step2: PC Term 2
source ~/bashrc
ros2 run turtlebot3_teleop teleop_keyboard
Step1: PC Term 1
source ~/bashrc
ros2 run turtlesim turtlesim_node --ros-args -r /turtle1/cmd_vel:=/cmd_vel
NEED TO UPDATE

## Slide 44: Using TurtleSIM to test following logic
Step2: PC Term 2
source ~/bashrc
ros2 run turtlebot3_teleop teleop_keyboard
Step1: PC Term 1
source ~/bashrc
ros2 run turtlesim turtlesim_node --ros-args -r /turtle1/cmd_vel:=/cmd_vel
Replace with your code

## Slide 45: Results & Code Review by each team
Show actual results against the expected results and explain the code generated

## Slide 46: Sprint 1&2 – Detection Alert/AMR Controller Integration & Test

## Slide 47: Expected outcome
Detection Alert and AMR Controller able to pass topics for necessary actions between

## Slide 48: Team Exercise 8
Perform integrate and test of Detection Alert and AMR Controller Modules

## Slide 49: Results & Code Review by each team
Show actual results against the expected results and explain the code written

## Slide 50: 프로젝트 rule number ONE!!!
Are we still having FUN!