## Slide 1: Good Morning! 早上好! 안녕하세요!
Day 3

## Slide 2: Day 1
Welcome
Project Introduction
Introduction to Project Development Process
Business Requirement Development
System Requirement Development
System(High Level) Design
Time Management

## Slide 3: Day 2 (Mini project)
Yolo객체 인식 모델 활용과 성능 평가 방법 이해
Custom Dataset과 Fine Tuning으로 자체 객체 인식 모델 구현 및 평가
(Optional)Segmentation,Tracking,경량화 모델 등 개별 요구사항에 적합한 모델 탐색 및 성능 검증
YOLOv8 기반 데이터 수집/학습/deploy (Detection Alert)
  감시용 데이터 수집(bus, truck, tank 등)
  감시용 데이터 라벨링
  YOLOv8 기반 학습
  YOLOv8 Object Detection
Porting to ROS
  Create Detection Alert Node
  Generate Topics to send image and Obj. Det. results
  Create Subscriber node and display image and print data from the Topic

## Slide 4: Day 3 (Mini project)
AMR(Autonomous Mobile Robot) Turtlebot4 개발 환경 구축
로봇 개발 환경에 완성 모델 서빙 및 테스트 / 로봇 H/W, 제반 환경의 한계점 도출
  Tracking 데이터 수집(bus, truck, tank 등)
  Tracking 데이터 라벨링
  YOLOv8 기반 학습
  YOLOv8 Object Tracking
Turtlebot4 시뮬레이션 환경 구축
  SLAM과 Map 생성 및 파라미터 튜닝(Localization, AMCL)
  AutoSLAM으로 맵 생성

## Slide 5: Day 4 (Mini project)
Turtlebot4 Navigation과 파라미터 튜닝(Local Costmap, Global Costmap)
Turtlebot4 API를 활용한 Initial Pose Navigate_to Pose 구현
Turtlebot4 API를 활용한 Navigate_Through_pose, Follow Waypoints 구현
로봇 개발 환경에 적용 및 테스트 / 로봇 H/W, 제반 환경의 한계점 도출
AMR기반 카메라 인식 autonomous driving 시스템 with obstacle avoidance 구축 (AMR Controller)
  Digital Mapping of environment
  Goal Setting and Obstacle Avoidance using Navigation
  Object Tracking w/ AMR camera
  Control logic between navigation/obj. tracking/ obj. following (teleop)
Porting to ROS
  Create AMR Controller Node
  Create and send Obj. Tracking Image and data to Sysmon
Integrate and test with Detection

## Slide 6: 프로젝트 rule number ONE!!!
Have Fun Fun Fun!

## Slide 9: SW Development Process
Agile-SPRINTs

## Slide 10: Project Sprints
Detection Alert
  Camera Capture
  Object Detection
  Send messages to other subsystems
AMR Controller
  Receive messages and act accordingly
  Move using (SLAM) with Obstruction avoidance
  Target Acquisition (Obj. Det.) and Tracking
  Follow target using camera and motor control
System Monitor
  Receive and Display Detection Camera and info
  Receive and Display AMR Camera and info
  Store, display, and report Information and Alerts

## Slide 11: Team Exercise 5
Perform coding and testing of Detection Alert Module

## Slide 12: Results & Code Review by each team
Show actual results against the expected results and explain the code written

## Slide 13: Project Sprints
Detection Alert
  Camera Capture
  Object Detection
  Send messages to other subsystems
AMR Controller
  Receive messages and act accordingly
  Move using (SLAM) with Obstruction avoidance
  Target Acquisition (Obj. Det.) and Tracking
  Follow target using camera and motor control
System Monitor
  Receive and Display Detection Camera and info
  Receive and Display AMR Camera and info
  Store, display, and report Information and Alerts

## Slide 14: Running Obj. Det on a real robot

## Slide 15: AMR Introduction
User Manual · Turtlebot4 User Manual
https://turtlebot.github.io/turtlebot4-user-manual/

## Slide 17: Setup PC for AMR
Turtlebot4 PC Setup
https://indecisive-freedom-6e8.notion.site/Turtlebot4-PC-Setup-1d98e215779c80e887b6c1dff4f151be

## Slide 18: Power on and off AMR
로봇 전원 켜기
TurtleBot 4를 도크에 놓기
도크의 녹색 LED가 몇 초 동안 켜지고 TurtleBot 4가 켜집니다. 로봇이 부팅될 때까지 잠시 기다리세요.
로봇 버튼과 표시등에 대한 자세한 내용은 Create®3 설명서를 참조하세요.
Power off
Turtlebot4 를 도크에서 불리 하기
신호음이 들릴 때까지 Create3의 전원 버튼을 5초 동안 길게 누릅니다.
전원 버튼을 놓습니다.

## Slide 19: Connecting to AMR -- SSH
Connect your PC to WiFi router that your AMR is connected
Ex: RokeyAP_Test
Obtain the ip address shown on the OLED display of the Turtlebot4
EX: 192.168.10.16
Open a terminal window
dpkg -l | grep openssh
If not installed…
sudo apt install openssh-server –y
Connect to AMR via SSH
ssh ubuntu@192.168.10.16
  PW: rokey1234
Do NOT INSTALL any packages to AMR WITHOUT speaking with me first!!!

## Slide 20: How to SETUp AMR
Turtlebot4 Setup
https://indecisive-freedom-6e8.notion.site/Turtlebot4-Setup-1d98e215779c801b8e74eff67eb6305e

## Slide 21: How to TEST PC – AMR Connection
ros2 topic list (will need to execute it twice)
  #Check the list
ros2 run teleop_twist_keyboard teleop_twist_keyboard --ros-args -r /cmd_vel:=/robot <n>/ /cmd_vel

## Slide 22: Object Tracking with AMR Camera

## Slide 23: Coding Hints
Image Capture

## Slide 24: Coding Hints
Image Capture
Data Labelling
  labelImg

## Slide 25: Coding Hints
Data Labelling : use previously installed LabelImg
Or
pip3 install labelImg
  May also need “pip3 install PyQt5 lxml”
labelImg

## Slide 26: Coding Hints
Data Labelling : LabelImg

## Slide 27: Coding Hints
Image Capture
Data Labelling
Data Preprocessing

## Slide 28: Zip train data Set

## Slide 29: Using google Collab. To create custom model

## Slide 30: Perform Yolo Training & Inference for AMR Controller

## Slide 31: Undock/dock amr
undock
ros2 topic list
  Check the list
ros2 action send_goal /robot<n>/undock irobot_create_msgs/action/Undock “{}”
dock
ros2 topic list
  Check the list
ros2 action send_goal /robot<n>/dock irobot_create_msgs/action/Dock “{}”

## Slide 32: Coding Hints
Image Capture
Data Labelling
Preprocessing
Yolo8 Object Det

## Slide 33: Running in simulation

## Slide 34: operating a robot(SIM)
Term1
ros2 launch turtlebot4_ignition_bringup turtlebot4_ignition.launch.py rviz:=true
Term2
ros2 topic list
ros2 topic echo <topic> --once
  /oakd/rgb/preview/image_raw
  /oakd/rgb/preview/depth
  ….

## Slide 35: Setup Nvidia gpu for slam

## Slide 36: digital Mapping using SLAM (SIM)
Term1
ros2 launch turtlebot4_ignition_bringup turtlebot4_ignition.launch.py nav2:=true slam:=true rviz:=true
Term2 (save map after mapping finishes)
ros2 service call /slam_toolbox/save_map slam_toolbox/srv/SaveMap "name: data: 'map_name’”
  Ex:: ros2 service call /slam_toolbox/save_map slam_toolbox/srv/SaveMap "name: data: ‘my_map'"

## Slide 37: digital Mapping with Auto – SLAM (SIM)
Term1
ros2 launch turtlebot4_ignition_bringup turtlebot4_ignition.launch.py nav2:=true slam:=true rviz:=true
Undock the robot
Term3 (save map after mapping finishes)
ros2 service call /slam_toolbox/save_map slam_toolbox/srv/SaveMap "name: data: 'map_name’”
  Ex:: ros2 service call /slam_toolbox/save_map slam_toolbox/srv/SaveMap "name: data: ‘my_map'"
Term2
ros2 launch explore_lite explore.launch.py

## Slide 38: Auto slam concept/algorithm

## Slide 39: Algorithm Detail
Map Subscription
explore_lite subscribes to the SLAM-generated occupancy grid (/map topic) and identifies:
  Free space: known, unoccupied areas
  Occupied space: obstacles
  Unknown space: unexplored
Frontier Detection
The map is scanned for cells that:
  Are free, and
  Are adjacent to at least one unknown cell.
These are marked as frontier cells.

## Slide 40: Algorithm detail
Frontier Grouping
  Frontier cells are clustered into connected regions.
  Each group represents a potential exploration target.
Goal Selection
  For each frontier group, a representative point (typically the centroid or closest point) is selected.
  The robot scores each group based on:
    Distance from the robot
    Information gain (how much new area might be revealed)
  The best-scoring frontier is chosen as the next goal.

## Slide 41: Algorithm detail
Termination
  While (frontiers exist and reachable)
  Select best frontier
  Send as goal
  If goal fails → blacklist
  If (no frontiers or all blacklisted)
  Terminate exploration

## Slide 42: Checking Digital Map (SIM)
Check if correct
xdg-open <map-path>/map.pgm
Or,
eog <map-path>/map.pgm

## Slide 43: Navigation w/ Digital map (SIM)
Term1
ros2 launch turtlebot4_ignition_bringup turtlebot4_ignition.launch.py nav2:=true slam:=false localization:=true rviz:=true

## Slide 44: Parameter tuning???
slam
navigation
NEED TO UPDATE

## Slide 45: Tutorial(sim)
TurtleBot 4 Navigator · User Manual
  https://turtlebot.github.io/turtlebot4-user-manual/tutorials/turtlebot4_navigator.html
Terminal 1
ros2 launch turtlebot4_ignition_bringup turtlebot4_ignition.launch.py nav2:=true slam:=false localization:=true rviz:=true
Terminal 2
ros2 run turtlebot4_python_tutorials nav_to_pose
ros2 run turtlebot4_python_tutorials nav_through_poses
ros2 run turtlebot4_python_tutorials follow_waypoints
ros2 run turtlebot4_python_tutorials create_path
ros2 run turtlebot4_python_tutorials mail_delivery
ros2 run turtlebot4_python_tutorials patrol_loop

## Slide 46: Using Depth (SIM)

## Slide 47: 프로젝트 rule number ONE!!!
Are we still having FUN!